G-217 Bluetooth Audio Dongle 
USER GUIDE

Charge the audio adaptor via travel charger or USB cable

The Bluetooth audio dongle is rechargeable and must be charged before use.

- Plug the DC jack on the charger to the charging port of G-217 and plug the charger adaptor into an electrical outlet.

- The battery is fully charged when the red light goes off.

LED Display

- Red LED status indicator: R-LED

- Green LED status indicator: G-LED

- Standby mode: G-LED flash.

- Battery low: R-LED flash.

- Charging: G-LED flash, R-LED constant on.

- Off mode: None LED flash.

- Pairing mode: G-LED and R-LED flash alternately.

- Active mode: G-LED constant on.

(

Start to use

‧Turn on / Turn off the audio adaptor

- To turn on the adaptor, press the on/off button for 2-3 seconds, you will see that
G-LED flashed fast for 1.5 seconds, then keeps flashing slowly.

- To turn off the adaptor, press the on/off button for 2-3 seconds, you will see that
R-LED flashes fast for 1.5 seconds, then both G-LED and R-LED are off.

‧To pair your headset with the adaptor

- Ensure the adaptor is power-charged and make the adaptor on off mode.

- Press the on/off button for more than 6 seconds until you see that G-LED and R-LED both flash alternately, then release the on/off button to leave the adaptor on pairing mode.

- Refer to your headset’s user guide and set your headset into pairing mode..

- And then both the audio adaptor and your headset will automatically search and pair with each other.  When the LED indicator on the audio dongle turn from G-LED and R-LED flash to leave only G-LED flash and your headset also turn into standby mode, that will mean both devices are paired successfully.

- To make sure if this audio adaptor is successfully paired with your headset, please short press the on/off button once on the audio adaptor.  If the G-LED on the audio dongle turn from flash to constant on, then means it’s really successfully paired with your headset and you can press the on/off button on the audio adaptor to turn both audio adaptor and your headset from active mode to standby mode for saving battery power.

‧To “ Make “, “Answer” and “End” calls

- To make or answer calls, just short press the answer button once from your headset first.  This is to turn your headset from “ standby “ to “ active “ mode and turning on the audio link between your headset and the audio adaptor. (It may take about 1 second for the audio link to start.)

- You will then need to dial or answer the call by using the phone keypad.

- When you finish the call, short press the on/off button on your headset to cut the audio link and return to standby mode.

- Last, use the phone keypad to end the call.

* If your phone support auto answering function, you can set your phone on auto answering mode.  In this case, when the call comes, just short press the on/off button on your headset to active link with the audio adaptor and short press the on/off button again to finish call and cut the audio link.  Do not need to press any button on your phone keypad to answer or end the call.

(